## Slide 1: In-situ OAM Direct Exporting
draft-ioamteam-ippm-ioam-direct-export-00
Haoyu Song, Barak Gafni, Tianran Zhou, Zhenbin Li,
Frank Brockners, Shwetha Bhandari, Ramesh Sivakolundu, Tal Mizrahi
IETF 106, Singapore
November 2019

## Slide 2: The History of This Draft
This draft combines two somewhat similar approaches:
  The PBT-I concept from draft-song-ippm-postcard-based-telemetry
  The Immediate Export flag from draft-mizrahi-ippm-ioam-flags
The decision in IETF 105 was to combine them.
This draft is the product of a design team that worked on combining the two concepts.
October 2019 - draft 00.
IETF 106, Nov 2019

## Slide 3: Direct Exporting (DEX) – Overview
^
|Exported IOAM data
|
|
|
+--------------+------+-------+--------------+
| | | |
| | | |
User +---+----+ +---+----+ +---+----+ +---+----+
packets |Encapsu-| | Transit| | Transit| |Decapsu-|
--------->|lating |====>| Node |====>| Node |====>|lating |---->
|Node | | A | | B | |Node |
+--------+ +--------+ +--------+ +--------+
Insert DEX Export Export Remove DEX
option and IOAM data IOAM data option and
export data export data
IOAM data is exported without modifying data packets.
Simplifies transit node processing.
Reduces the data plane on-the-wire overhead of IOAM.
IETF 106, Nov 2019

## Slide 4: The Direct Exporting (DEX) Option
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Namespace-ID | Flags |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| IOAM-Trace-Type | Reserved |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Flow ID (optional) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sequence Number (Optional) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
A new IOAM option that indicates that IOAM data is exported to a collector.
IOAM-Trace-Type indicates which data fields are exported.
Two optional fields.
IETF 106, Nov 2019

## Slide 5: Example: The DEX Option as an IPv6 Extension Header
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Option Type | Opt Data Len | Reserved | IOAM Type |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Namespace-ID | Flags |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| IOAM-Trace-Type | Reserved |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Flow ID (optional) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sequence Number (Optional) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
The IOAM IPv6 extension header is defined in: draft-ietf-ippm-ioam-ipv6-options-00 (work in progress).
IOAM Type indicates this is a DEX option.
Opt Data Len indicates whether the optional fields are present.
IETF 106, Nov 2019

## Slide 6: Summary and Next Steps
Based on the input from the working group, this draft presents a consolidated approach.
The draft is stable.
Ready for working group adoption.
IETF 106, Nov 2019