## Slide 1: In-situ OAM Direct Exporting
draft-ietf-ippm-ioam-direct-export-00
Haoyu Song, Barak Gafni, Tianran Zhou, Zhenbin Li,
Frank Brockners, Shwetha Bhandari, Ramesh Sivakolundu, Tal Mizrahi
IETF, IPPM Interim,
April 2020

## Slide 2: Direct Exporting (DEX) – Overview
^
|Exported IOAM data
|
|
|
+--------------+------+-------+--------------+
| | | |
| | | |
User +---+----+ +---+----+ +---+----+ +---+----+
packets |Encapsu-| | Transit| | Transit| |Decapsu-|
--------->|lating |====>| Node |====>| Node |====>|lating |---->
|Node | | A | | B | |Node |
+--------+ +--------+ +--------+ +--------+
Insert DEX Export Export Remove DEX
option and IOAM data IOAM data option and
export data export data
IOAM data is exported without modifying data packets.
Simplifies transit node processing.
Reduces the data plane on-the-wire overhead of IOAM.
IPPM Interim, April 2020

## Slide 3: The History / State of this Draft
This draft combines two somewhat similar approaches:
  The PBT-I concept from draft-song-ippm-postcard-based-telemetry
  The Immediate Export flag from draft-mizrahi-ippm-ioam-flags
This draft is the product of a design team that worked on combining the two concepts.
December 2019 – adopted by the IPPM WG.
February 2019 – draft-ietf-00.
IPPM Interim, April 2020

## Slide 4: Open Issue – Hop Count
Question: should the DEX option include an explicit Hop Count field, or is the Hop_Lim/Node_ID data field sufficient?
No Hop Count:
  Using existing functionality: Hop_Lim/Node_ID data field can be used, copied from the TTL/Hop Limit from the lower layer, and included in the exported packet.
  The DEX option does not need to be modified by transit switches.
Explicit Hop Count:
  The lower layer TTL may not be accurate, e.g., L2 or hierarchical VPN.
  Allows to detect IOAM-capable node that fails to export packets.
IPPM Interim, April 2020