## Slide 1: In-situ OAM (IOAM) draft-ietf-ippm-ioam-data-01
Frank Brockners, Shwetha Bhandari, Carlos Pignataro (Cisco) Hannes Gedler (rtbrick), Steve Youell (JPMC), John Leddy (Comcast) David Mozes (Mellanox), Tal Mizrahi (Marvell), Petr Lapukhov (Facebook) Remy Chang (Barefoot), Daniel Bernier (Bell Canada), John Lemon (Broadcom)
IETF 100 – IPPM; November 13, 2017

## Slide 2: Updates between -00 and -01 version
Overflow indication and max value for time data fields
  “If the transit delay exceeds 2^31-1 nanoseconds then the top bit 'O' is set to indicate overflow and value set to 0x80000000”
Follow IETF convention is that bit 0 is the most significant bit
  Flags field – O-bit (Overflow bit)
  Fixed examples in section 4.1.4. (Examples of IOAM node data)
See also: https://github.com/inband-oam/ietf/issues?q=is%3Aissue+is%3Aclosed

## Slide 3: Discussion topics
Node data length does not include opaque state snapshot length
  Proposed by Mickey Spiegel: https://github.com/inband-oam/ietf/pull/60/commits/77725d2ff5d7ab7d0fd384c3d5a89faa77309202
  This is a bug and we‘ll reflect it in the next rev

## Slide 4: Discussion topics
Timestamp format
  Proposed by John Lemon: https://mailarchive.ietf.org/arch/msg/ippm/kg1hQTrnz_VL7oRp4ffZmpgZbJo
  Extend the timestamp to allow it to support both PTP and NTP
    The seconds portion would remain largely as is, although the seconds would obviously use different epochs, depending upon which type of timestamp is used within the in-situ OAM domain
    The datatype currently named nanoseconds would be renamed to sub-seconds and would either carry nanoseconds or fractional seconds, for PTP or NTP, respectively
  Change current timestamp related code points for IOAM-Trace-Type and add two new ones:
    CHANGE: Bit 2 When set indicates presence of PTP timestamp seconds in the node data
    CHANGE: Bit 3 When set indicates presence of PTP timestamp nanoseconds in the node data
    NEW: Bit 12 When set indicates presence of NTP timestamp seconds in the node data
    NEW: Bit 13 When set indicates presence of NTP timestamp fractional seconds in the node data

## Slide 5: Discussion topics
New Edge-to-Edge data types
  Proposed by John Lemon: https://mailarchive.ietf.org/arch/msg/ippm/kg1hQTrnz_VL7oRp4ffZmpgZbJo
  Add a few Edge-To-Edge data types
    In addition to the currently defined 64-bit sequence number, add a sequence number taking up only 32 bits
    Add same timestamp types as used by Hop-By-Hop to measure delay (and delay variation) across the entire path, without having to use the Hop-By-Hop timestamps to measure at every node in the path