## Slide 1: In-situ OAM Direct Exporting
draft-ioamteam-ippm-ioam-direct-export-00
Haoyu Song, Barak Gafni, Tianran Zhou, Zhenbin Li,
Frank Brockners, Shwetha Bhandari, Ramesh Sivakolundu, Tal Mizrahi
IETF 106, Singapore
November 2019

## Slide 2: The History of This Draft
This draft combines two somewhat similar approaches:
  The PBT-I concept from draft-song-ippm-postcard-based-telemetry
  The Immediate Export flag from draft-mizrahi-ippm-ioam-flags
The decision in IETF 105 was to combine them.
This draft is the product of a design team that worked on combining the two concepts.
October 2019 - draft 00.
IETF 106, Nov 2019

## Slide 3: Direct Exporting (DEX) – Overview
+-----------+
| Telemetry |
| Data |
| Collector |
+-----------+
^
|Exported IOAM data
|
|
|
+--------------+------+-------+--------------+
| | | |
| | | |
User +---+----+ +---+----+ +---+----+ +---+----+
packets |Encapsu-| | Transit| | Transit| |Decapsu-|
--------->|lating |====>| Node |====>| Node |====>|lating |---->
|Node | | A | | B | |Node |
+--------+ +--------+ +--------+ +--------+
Insert DEX Export Export Remove DEX
option and IOAM data IOAM data option and
export data export data
IOAM data is exported to a collector without modifying data packets.
Simplifies transit node processing.
Reduces the data plane on-the-wire overhead of IOAM.
IETF 106, Nov 2019

## Slide 4: The Direct Exporting (DEX) Option
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Namespace-ID | Flags |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| IOAM-Trace-Type | Reserved |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Flow ID (optional) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sequence Number (Optional) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
A new IOAM option that indicates that IOAM data is exported to a collector.
IOAM-Trace-Type indicates which data fields are exported.
Two optional fields.
IETF 106, Nov 2019

## Slide 5: Example: The DEX Option as an IPv6 Extension Header
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Option Type | Opt Data Len | Reserved | IOAM Type |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Namespace-ID | Flags |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| IOAM-Trace-Type | Reserved |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Flow ID (optional) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sequence Number (Optional) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
The IOAM IPv6 extension header is defined in: draft-ietf-ippm-ioam-ipv6-options-00 (work in progress).
IOAM Type indicates this is a DEX option.
Opt Data Len indicates whether the optional fields are present.
IETF 106, Nov 2019

## Slide 6: Open Issue: Hop Limit / Hop Count
The collector may use the hop count of each exported packet in order to reconstruct the path and detect missing exported packets.
IETF 106, Nov 2019
+-----------+
| Telemetry |
| Data |
| Collector |
+-----------+
^
|Exported IOAM data
|
|
|
+--------------+------+-------+--------------+
| | | |
| | | |
User +---+----+ +---+----+ +---+----+ +---+----+
packets |Encapsu-| | Transit| | Transit| |Decapsu-|
--------->|lating |====>| Node |====>| Node |====>|lating |---->
|Node | | A | | B | |Node |
+--------+ +--------+ +--------+ +--------+
Hop Limit:
62
61
60
59

## Slide 7: Open Issue: Hop Limit / Hop Count
Approach 1:
  Use the Hop_Lim/Node_ID data field.
  This data field is already defined in draft-ietf-ippm-ioam-data.
Approach 2:
  Use a dedicated Hop Limit field in the DEX option.
  Increment by each transit node.
IETF 106, Nov 2019
  ✔ Does not require transit nodes to modify data packets.
  ✔ Reuses an existing data field.
  ✔ Detects missing exported packets when there are IOAM-incapable transit nodes.
  ✔ Applicable in scenarios in which the lower layer TTL is not available.

## Slide 8: Next Steps
Request working group adoption.
IETF 106, Nov 2019

## Slide 9: Backup

## Slide 10: Open Issue: Hop Limit / Hop Count
IETF 106, Nov 2019
  Missing exported packets when there are IOAM-incapable transit nodes:
+-----------+
| Telemetry |
| Data |
| Collector |
+-----------+
^
|Exported IOAM data
|
|
|
+--------------+------+-------+--------------+
| | | |
| | | |
User +---+----+ +---+----+ +---+----+ +---+----+
packets |Encapsu-| | Transit| |Non-IOAM| |Decapsu-|
--------->|lating |====>| Node |====>| Router |====>|lating |---->
|Node | | A | | | |Node |
+--------+ +--------+ +--------+ +--------+
IP Hop Limit:
62
61
60
59
Dedicated Hop Count:
1
2
3