## Slide 1: In-situ OAM (IOAM) in VXLAN-GPE draft-brockners-ioam-vxlan-gpe-00
Frank Brockners, Shwetha Bhandari, Vengada Prasad Govindan, Carlos Pignataro (Cisco) Hannes Gedler (rtbrick), Steve Youell (JPMC), John Leddy (Comcast) David Mozes (Mellanox), Tal Mizrahi (Marvell), Petr Lapukhov (Facebook) Remy Chang (Barefoot), Daniel Bernier (Bell Canada)
IETF 100 – LISP; November, 2017

## Slide 2: In-situ OAM in a nutshell
Gather telemetry and OAM information along the path within the data packet, (hence “in-situ OAM”) as part of an existing/additional header
  No extra probe-traffic (as with ping, trace, ..)
  “Hybrid, Type-1 OAM” per RFC 7799
Generic, Transport independent data-fields for IOAM
  Scope: Per-hop, specific-hops only, end-to-end
  Data fields include: Node IDs, interface IDs, timestamps, sequence numbers, ...
Encapsulation
  IOAM data fields can be embedded into a variety of transports, including: IPv6, SRv6, NSH, GRE, Geneve, VXLAN-GPE ...
Base IOAM document adopted by IPPM!
  draft-ietf-ippm-ioam-data-01
Hdr
OAM
Payload
IOAM domain
Node-ID,..
Ingress/Egress I/F, ..
Timestamp, Delay,..
Proof of Transit
Sequence number
Generic customer data

## Slide 3: IOAM over VXLAN-GPE (draft-brockners-ioam-vxlan-gpe-00)
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Outer Ethernet Header |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Outer IP Header |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Outer UDP Header |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+--+
|R|R|Ver|I|P|R|O| Reserved | NP=IOAM_Trace | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ GPE
| Virtual Network Identifier (VNI) | Reserved | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+--+
| Type | IOAM HDR len| Reserved | Next Protocol | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ IOAM
| IOAM-Trace-Type |NodeLen| Flags | Max Length | Trace
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
| | |
| node data list [0] | IOAM
| | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ D
| | a
| node data list [1] | t
| | a
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ ... ~ S
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ p
| | a
| node data list [n-1] | c
| | e
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |
| | |
| node data list [n] | |
| | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-<--+
| |
| |
| Payload + Padding (L2/L3/ESP/...) |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
VXLAN-GPE header
IOAM shim header for VXLAN-GPE
Specifies the next protocol Allows multiple data field

## Slide 4: Open Questions
Section 4: Discussion of the encapsulation approach
  An encapsulation of IOAM data fields in VXLAN-GPE should be friendly to an implementation in both hardware as well as software forwarders and support a wide range of deployment cases, including large networks that desire to leverage multiple IOAM data fields at the same time.
“To nest TLVs or not to”?, Single GPE protocol type for all IOAM data categories (trace, proof-of-transit, and edge-to-edge) or one GPE protocol type per IOAM data category?
  “Next header” approach: Single GPE protocol type for all IOAM types: Results in serial list of IOAM data categories. Avoids iterative lookups. Finding the L4 header requires parsing each header of the list. Current approach in -00 version of the draft.
  “TLV” approach: One GPE protocol type per IOAM category: Results in nested TLVs. Requires iterative lookups. Single length field for all options allows nodes not interested in the IOAM information to skip the information easily.
vs.

## Slide 5: Status and next steps
Data Fields for In-situ OAM
  Adopted by IPPM
  draft-ietf-ippm-ioam-data
IOAM encapsulations into protocols
  draft-brockners-nvo3-ioam-geneve-00
  draft-brockners-ioam-vxlan-gpe-00 (this discussion)
  draft-brockners-sfc-ioam-nsh-00
  … more to come…
IOAM in VXLAN-GPE in LISP WG
  Feedback from LISP WG appreciated, especially on open questions
  WG adoption?