## Slide 1: In-situ OAM (IOAM) in NSH (and POT) draft-brockners-sfc-ioam-nsh-00 draft-brockners-proof-of-transit-04
Frank Brockners, Shwetha Bhandari, Vengada Prasad Govindan, Carlos Pignataro (Cisco) Hannes Gedler (rtbrick), Steve Youell (JPMC), John Leddy (Comcast) David Mozes (Mellanox), Tal Mizrahi (Marvell), Petr Lapukhov (Facebook) Remy Chang (Barefoot), Daniel Bernier (Bell Canada)
IETF 100 – SFC WG; November, 2017

## Slide 2: In-situ OAM in a nutshell
Gather telemetry and OAM information along the path within the data packet, (hence “in-situ OAM”) as part of an existing/additional header
  No extra probe-traffic (as with ping, trace, ..)
  “Hybrid, Type-1 OAM” per RFC 7799
Generic, Transport independent data-fields for IOAM
  Scope: Per-hop, specific-hops only, end-to-end
  Data fields include: Node IDs, interface IDs, timestamps, sequence numbers, ...
Encapsulation
  IOAM data fields can be embedded into a variety of transports, including: IPv6, SRv6, NSH, GRE, Geneve, VXLAN-GPE ...
Base IOAM document adopted by IPPM!
  draft-ietf-ippm-ioam-data-01
Hdr
OAM
Payload
IOAM domain
Node-ID,..
Ingress/Egress I/F, ..
Timestamp, Delay,..
Proof of Transit
Sequence number
Generic customer data

## Slide 3: IOAM over NSH (draft-brockners-sfc-ioam-nsh-00)
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
|Ver|O|C|R|R|R|R|R|R| Length | MD Type | NP=IOAM_Trace | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ N
| Service Path Identifer | Service Index | S
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ H
| ... | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
| Type | IOAM HDR len| Reserved | Next Protocol | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ IOAM
| IOAM-Trace-Type |NodeLen| Flags | Octets-left | Trace
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
| | |
| node data list [0] | IOAM
| | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ D
| | a
| node data list [1] | t
| | a
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ ... ~ S
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ p
| | a
| node data list [n-1] | c
| | e
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |
| | |
| node data list [n] | |
| | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-<--+
| |
| |
| Payload + Padding (L2/L3/ESP/...) |
| |
| |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
NSH header
IOAM shim header for NSH
Specifies the next protocol Allows multiple data field

## Slide 4: Open Questions
Section 4: Discussion of the encapsulation approach
  An encapsulation of IOAM data fields in NSH should be friendly to an implementation in both hardware as well as software forwarders and support a wide range of deployment cases, including large networks that desire to leverage multiple IOAM data fields at the same time.
“To nest TLVs or not to”?, i.e. use MD Type 2 to encapsulate IOAM data categories (trace, proof-of-transit, and edge-to-edge) or use the next header approach
  “Next header” approach: Results in serial list of IOAM data categories. Avoids iterative lookups. Finding the L4 header requires parsing each header of the list. Current approach in -00 version of the draft.
  “TLV” approach using MD Type 2: Results in nested TLVs. Requires iterative lookups. Single length field for all options allows nodes not interested in the IOAM information to skip the information easily. Approach taken by the VPP open source implementation
Total length of IOAM data? MD Type 2 offers 6 bits for length = 256 of encap data
Setting the ‘O’ bit Should the ‘O’ bit be set in packets that include IOAM metadata?
vs.

## Slide 5: What about compliance?
How do we ensure the integrity of a path or service chain?
draft-brockners-proof-of-transit-04
Meta-data added to all user traffic
  Based on “Share of a secret”
  Updated at every hop where proof of transit is required
Verifier checks whether collected meta-data allows retrieval of secret
  “Proof of Transit”: Path verified
Referenced from NSH!
Controller
Secret
X
B
C
A
Verifier

## Slide 6: Status
Data Fields for In-situ OAM
  Adopted by IPPM
  draft-ietf-ippm-ioam-data-01
IOAM encapsulations into protocols
  draft-brockners-nvo3-ioam-geneve-00
  draft-brockners-ioam-vxlan-gpe-00
  draft-brockners-sfc-ioam-nsh-00 (this discussion)
  … more to come…

## Slide 7: Next steps
IOAM in NSH in SFC WG
  Feedback from SFC WG appreciated, especially on open questions
  WG adoption?
IOAM Proof of Transit
  Consider WG adoption