## Slide 1: In-situ OAM (IOAM) in Geneve draft-brockners-nvo3-ioam-geneve-00
Frank Brockners, Shwetha Bhandari, Vengada Prasad Govindan, Carlos Pignataro (Cisco) Hannes Gedler (rtbrick), Steve Youell (JPMC), John Leddy (Comcast) David Mozes (Mellanox), Tal Mizrahi (Marvell), Petr Lapukhov (Facebook) Remy Chang (Barefoot), Daniel Bernier (Bell Canada)
IETF 100 – NVO3; July, 2017

## Slide 2: In-situ OAM in a nutshell
Gather telemetry and OAM information along the path within the data packet, (hence “in-situ OAM”) as part of an existing/additional header
  No extra probe-traffic (as with ping, trace, ..)
  “Hybrid, Type-1 OAM” per RFC 7799
Generic, Transport independent data-fields for IOAM
  Scope: Per-hop, specific-hops only, end-to-end
  Data fields include: Node IDs, interface IDs, timestamps, sequence numbers, ...
Encapsulation
  IOAM data fields can be embedded into a variety of transports, including: IPv6, SRv6, NSH, GRE, Geneve, VXLAN-GPE ...
Hdr
OAM
Payload
IOAM domain
Node-ID,..
Ingress/Egress I/F, ..
Timestamp, Delay,..
Proof of Transit
Sequence number
Generic customer data

## Slide 3: IOAM over Geneve (draft-brockners-nvo3-ioam-geneve-00)
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+--+
|Ver| Opt Len |O|C| Rsvd. | Protocol Type | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ Hdr
| Virtual Network Identifier (VNI) | Reserved | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+--+
| Option Class = IOAM_Trace | Type (incr.) |R|R|R| Length | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ IOAM
| IOAM-Trace-Type |NodeLen| Flags | Max Length | Trace
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
| | |
| node data list [0] | IOAM
| | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ D
| | a
| node data list [1] | t
| | a
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ ... ~ S
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ p
| | a
| node data list [n-1] | c
| | e
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |
| | |
| node data list [n] | |
| | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-<--+
| |
| |
| Payload + Padding (L2/L3/ESP/...) |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Geneve header
Geneve tunnel option
Option Class and Type specify which data field resides in the option.

## Slide 4: Open Questions
Section 4: Discussion of the encapsulation approach
  An encapsulation of IOAM data fields in Geneve should be friendly to an implementation in both hardware as well as software forwarders and support a wide range of deployment cases, including large networks that desire to leverage multiple IOAM data fields at the same time.
Tunnel option length field:
  Geneve tunnel option limits length to 128 bytes, which limits the range of deployment cases.
Metadata approach discussion:
  Use of the Geneve tunnel option requires iterative lookups (nested TLVs) which present a challenge for some hardware implementations.
  Single length field for all options allows nodes not interested in the IOAM information to skip the information easily. I.e. no need for parsing each header of the list to find the L4 header.
vs.

## Slide 5: Status and next steps
Data Fields for In-situ OAM
  Adopted by IPPM
  draft-ietf-ippm-ioam-data
IOAM encapsulations into protocols
  draft-brockners-nvo3-ioam-geneve-00 (this discussion)
  draft-brockners-ioam-vxlan-gpe-00
  draft-brockners-sfc-ioam-nsh-00
  … more to come…
IOAM in Geneve in NVO3 WG
  Feedback from NVO3 WG appreciated, especially on open questions
  WG adoption?